## Slide 1: Virtual Networking

## Slide 2: Azure Networking Components
Virtual Network
Subnets
NICs
NSGs
Load Balancer
Public IP
Traffic Manager

## Slide 3: Virtual Network
It is a representation of your own network in the cloud.
It is a logical isolation of the Azure cloud dedicated to your subscription.
Each VNet has its own CIDR block.

## Slide 4: Virtual Network
CIDR – Classless Interdomain Routing
10.0.0.0/16 – Address Space - 65536 IP Addresses
32 – 16 = 16
2 to the power 16 = 65536
10.0.0.0/24 – 256

## Slide 5: Private IP
10.0.0.0 – 10.255.255.255
172.16.0.0 - 172.31.255.255
192.168.0.0 - 192.168.255.255

## Slide 7: Subnets
Virtual network can be segmented into one or more subnets.
Subnets provide logical division within your networks

## Slide 8: Subnets
Service Requirement
Service Endpoints
Network Security Group – Zero or one network security group to each subnet

## Slide 9: IP Addressing and Endpoints

## Slide 10: IP Addressing
Communicate with other Azure resources, your on-premises network and internet.
Private IP – Communication within VNets
Public IP – Communication with internet or Azure Public facing services

## Slide 11: Public IP Address
Public IP Address | IP Address Association
Virtual Machine | NIC
Load Balancer | Front-end configuration
VPN Gateway | Gateway IP configuration
Application Gateway | Front-end configuration
SKU:
Basic
Standard

## Slide 12: Private IP Address
Public IP Address | IP Address Association
Virtual Machine | NIC
Internal Load Balancer | Front-end configuration
Application Gateway | Front-end configuration
10.0.0.0/16
Allocated – 10.0.0.4 – 10.0.0.9
Dynamic – 10.0.0.10
Static – 10.0.0.10 – 10.0.255.254